## Slide 1
Advance Networking
SUBJECT:
Advanced Java Programming
TOPIC:
Advance Networking
This work is licensed under a Creative Commons Attribution-NonCommercial-ShareAlike 4.0 International License. You are free to use, distribute and modify it, for noncommercial purposes only, provided you acknowledge the source.
Jatin Ambasana

## Slide 2: Agenda
Networking Basics
  TCP, UDP, Ports, DNS, Client-Server Model
TCP/IP in Java
Sockets
URL
  The java classes: URL, URLConnection
Datagrams

## Slide 3: JAVA NETWORKING
Java Networking is a concept of connecting two or more computing devices together so that we can share resources.
Java socket programming provides facility to share data between different computing devices.
Advantage of Java Networking : Sharing resources

## Slide 4: Java Networking Terminology
The widely used java networking terminologies are given below:
  IP Address : IP address is a unique number assigned to a node of a network e.g. 192.168.0.1 . It is composed of octets that range from 0 to 255. It is a logical address that can be changed.
  Protocol : A protocol is a set of rules basically that is followed for communication. For example:
    TCP
    FTP
    Telnet
    SMTP
    POP etc.

## Slide 5: Java Networking Terminology
  Port Number : The port number is used to uniquely identify different applications. It acts as a communication endpoint between applications. The port number is associated with the IP address for communication between two applications.
  MAC Address : MAC (Media Access Control) Address is a unique identifier of NIC (Network Interface Controller). A network node can have multiple NIC but each with unique MAC.
  Connection-oriented And Connection-less Protocol : In connection-oriented protocol, acknowledgement is sent by the receiver. So it is reliable but slow. The example of connection-oriented protocol is TCP. But, in connection-less protocol, acknowledgement is not sent by the receiver. So it is not reliable but fast. The example of connection-less protocol is UDP.
  Socket : A socket is an endpoint between two way communication

## Slide 6: The Network is Computer
Internet Server
PC client
Local Area Network
PDA

## Slide 7: Increased demand for Internet applications
To take advantage of opportunities presented by the Internet, businesses are continuously seeking new and innovative ways and means for offering their services via the Internet.
This created a huge demand for software designers with skills to create new Internet-enabled applications or migrate existing/legacy applications on the Internet platform.
Object-oriented Java technologies—Sockets, threads, RMI, clustering, Web services-- have emerged as leading solutions for creating portable, efficient, and maintainable large and complex Internet applications.

## Slide 8: Elements of C-S Computing
Network
Request
Result
a client, a server, and network
Client
Server
Client machine
Server machine

## Slide 9: Networking Basics
Computers running on the Internet communicate with each other using either the Transmission Control Protocol (TCP) or the User Datagram Protocol (UDP)

## Slide 10: Java Socket Programming
Java Socket programming is used for communication between the applications running on different JRE.
Java Socket programming can be connection-oriented or connection-less.
Socket and ServerSocket classes are used for connection-oriented socket programming and DatagramSocket and DatagramPacket classes are used for connection-less socket programming.
The client in socket programming must know two information:
  IP Address of Server, and
  Port number

## Slide 11: DNS - Domain name system
The Domain Name system (DNS) associates various sorts of information with so-called domain names.
Most importantly, it serves as the "phone book" for the Internet by translating human-readable computer hostnames, e.g. www.example.com, into the IP addresses, e.g. 208.77.188.166, that networking equipment needs to deliver information.
It also stores other information such as the list of mail exchange servers that accept email for a given domain.

## Slide 12: Understanding Ports
The TCP and UDP protocols use ports to map incoming data to a particular process running on a computer.
Server
Port
TCP
TCP or UDP
port
port
port
port
app
app
app
app
port#
data
Data
Packet
Client
Port

## Slide 13: Understanding Ports
Port is represented by a positive (16-bit) integer value
Some ports have been reserved to support common/well known services:
  ftp 21/tcp
  telnet 23/tcp
  smtp 25/tcp
  login 513/tcp
User level process/services generally use port number value >= 1024

## Slide 14: Sockets
Sockets provide an interface for programming networks at the transport layer.
Network communication using Sockets is very much similar to performing file I/O
  In fact, socket handle is treated like file handle.
  The streams used in file I/O operation are also applicable to socket-based I/O
Socket-based communication is programming language independent.
  That means, a socket program written in Java language can also communicate to a program written in Java or non-Java socket program.

## Slide 15: Socket Communication
A server (program) runs on a specific computer and has a socket that is bound to a specific port. The server waits and listens to the socket for a client to make a connection request.
server
Client
Connection request
port

## Slide 16: Socket Communication
If everything goes well, the server accepts the connection. Upon acceptance, the server gets a new socket bounds to a different port. It needs a new socket (consequently a different port number) so that it can continue to listen to the original socket for connection requests while serving the connected client.
server
Client
Connection
port
port
port

## Slide 17: Transmission Control Protocol
A connection-based protocol that provides a reliable flow of data between two computers.
Provides a point-to-point channel for applications that require reliable communications.
  The Hypertext Transfer Protocol (HTTP), File Transfer Protocol (FTP), and Telnet are all examples of applications that require a reliable communication channel
Guarantees that data sent from one end of the connection actually gets to the other end and in the same order it was sent. Otherwise, an error is reported.

## Slide 18: User Datagram Protocol
A protocol that sends independent packets of data, called datagrams, from one computer to another with no guarantees about arrival. UDP is not connection-based like TCP and is not reliable:
  Sender does not wait for acknowledgements
  Arrival order is not guaranteed
  Arrival is not guaranteed
Used when speed is essential, even in cost of reliability
  e.g. streaming media, games, Internet telephony, etc.

## Slide 19: Ports
Data transmitted over the Internet is accompanied by addressing information that identifies the computer and the port for which it is destined.
  The computer is identified by its 32-bit IP address, which IP uses to deliver data to the right computer on the network. Ports are identified by a 16-bit number, which TCP and UDP use to deliver the data to the right application.

## Slide 20: Ports – Cont.
Port numbers range from 0 to 65,535 (16-bit)
  Ports 0 - 1023 are called well-known ports. They are reserved for use by well-known services:
    20, 21: FTP
    23: TELNET
    25: SMTP
    110: POP3
    80: HTTP

## Slide 21: Networking Classes in the JDK
Through the classes in java.net, Java programs can use TCP or UDP to communicate over the Internet.
  The URL, URLConnection, Socket, and ServerSocket classes all use TCP to communicate over the network.
  The DatagramPacket, DatagramSocket, and MulticastSocket classes are for use with UDP.

## Slide 22: Networking Classes in the JDK
InetAddress
Socket and ServerSocket Class
URL class

## Slide 23: TCP/IP in Java
Accessing TCP/IP from Java is straightforward. The main functionality is in the following classes:
  java.net.InetAddress : Represents an IP address (either IPv4 or IPv6) and has methods for performing DNS lookup (next slide).
  java.net.Socket : Represents a TCP socket.
  java.net.ServerSocket : Represents a server socket which is capable of waiting for requests from clients.

## Slide 24: InetAddress
The InetAddress class is used to encapsulate both the numerical IP address and the domain name for that address.
We interact with this class by using the name of an IP host, which is more convenient and understandable than its IP address.
The InetAddress class hides the number inside.

## Slide 25: Factory Methods
static InetAddress getLocalHost( )
throws UnknownHostException
static InetAddress getByName(String hostName)
throws UnknownHostException
static InetAddress[ ] getAllByName(String hostName)
throws UnknownHostException

## Slide 26: Example:
class InetAddressTest1
{
public static void main(String args[])
throws UnknownHostException
{
InetAddress Address = InetAddress.getLocalHost();
System.out.println(Address);
Address =
InetAddress.getByName("www.google.com");
System.out.println(Address);
InetAddress SW[] =
InetAddress.getAllByName("www.yahoo.com");
for (int i=0; i<SW.length; i++)
System.out.println(SW[i]);
}
}

## Slide 27: Instance Methods
class InetAddressTest2
{
public static void main(String args[])
throws UnknownHostException
{
InetAddress Address =
InetAddress.getByName("www.google.com");
System.out.println(Address.getHostAddress());
System.out.println(Address.getHostName());
if(Address.isMulticastAddress())
System.out.println("It is multicast address");
}
}

## Slide 28: Sockets and Java Socket Classes
A socket is an endpoint of a two-way communication link between two programs running on the network.
A socket is bound to a port number so that the TCP layer can identify the application that data destined to be sent.
Java’s .net package provides two classes:
  Socket – for implementing a client
  ServerSocket – for implementing a server

## Slide 29: Java Sockets
ServerSocket(1234)
Socket(“128.250.25.158”, 1234)
Output/write stream
Input/read stream
It can be host_name like
“books.google.com” or “localhost”
Client
Server

## Slide 30: Client Sockets
Java wraps OS sockets (over TCP) by the objects of class java.net.Socket
Socket(String remoteHost,int remotePort)
Creates a TCP socket and connects it to the remote host on the remote port (hand shake)
Write and read using streams:
  InputStream getInputStream()
  OutputStream getOutputStream()

## Slide 31: Constructors
Socket(String remoteHost, int remotePort)
Socket(InetAddress ip, int remotePort)

## Slide 32: Instance Methods
InetAddress getInetAddress( )
int getPort( )
int getLocalPort( )
InputStream getInputStream( )
OutputStream getOutputStream( )
void close( )

## Slide 33: Socket class
Method | Description
1) public InputStream getInputStream() | returns the InputStream attached with this socket.
2) public OutputStream getOutputStream() | returns the OutputStream attached with this socket.
3) public synchronized void close() | closes this socket
A socket is simply an endpoint for communications between the machines. The Socket class can be used to create a socket.

## Slide 34: ServerSocket class
The ServerSocket class can be used to create a server socket.
This object is used to establish communication with the clients.
Method | Description
1) public Socket accept() | returns the socket and establish a connection between server and client.
2) public synchronized void close() | closes the server socket.

## Slide 35: Implementing a Client
1. Create a Socket Object:
client = new Socket( server, port_id );
2. Create I/O streams for communicating with the server.
is = new DataInputStream(client.getInputStream() );
os = new DataOutputStream( client.getOutputStream() );
3. Perform I/O or communication with the server:
  Receive data from the server:
String line = is.readLine();
  Send data to the server:
os.writeBytes("Hello\n");
4. Close the socket when done:
client.close();

## Slide 36: Example: Whois server
class Whois {
  public static void main(String args[ ]) throws Exception {
    int c;
    Socket s = new Socket("internic.net", 43);
    InputStream in = s.getInputStream();
    OutputStream out = s.getOutputStream();
    String str="www.google.com";
    byte buf[] = str.getBytes();
    out.write(buf);
    while ((c = in.read()) != -1)
    System.out.print((char) c);
    s.close();
  }
}

## Slide 37: Example: Time server
public class DayTime{
public static void main(String[] args) throws Exception {
Socket theSocket = new Socket("time.nist.gov", 13);
InputStream timeStream =theSocket.getInputStream();
StringBuffer time = new StringBuffer( );
int c;
while ((c = timeStream.read( )) != -1) time.append((char) c);
String timeString = time.toString( ).trim( );
System.out.println("It is " + timeString + " at " + "localhost");
}
}

## Slide 38: ServerSocket
This class implements server sockets. A server socket waits for requests to come in over the network. It performs some operation based on that request, and then possibly returns a result to the requester.
A server socket is technically not a socket: when a client connects to a server socket, a TCP connection is made, and a (normal) socket is created for each end point.

## Slide 39: Constructors
ServerSocket (int port)
throws BindException, IOException
ServerSocket (int port, int maxQueue)
throws BindException, IOException
ServerSocket (int port, int maxQ, InetAddress ip) throws IOException

## Slide 40: Implementing a Server
Open the Server Socket:
ServerSocket server;
DataOutputStream os;
DataInputStream is;
server = new ServerSocket( PORT );
Wait for the Client Request:
Socket client = server.accept();
Create I/O streams for communicating to the client
is = new DataInputStream(client.getInputStream() );
os = new DataOutputStream(client.getOutputStream());
Perform communication with client
Receive from client: String line = is.readLine();
Send to client: os.writeBytes("Hello\n");
Close sockets: client.close();

## Slide 41: Accepting Connections
Usually, the accept() method is executed within an infinite loop
  i.e., while(true){...}
The accept method returns a new socket (with a new port) for the new channel. It blocks until connection is made.
Syntax:
  Socket accept() throws IOException

## Slide 42: Client-Server Interaction via TCP

## Slide 43: Examples
Server1
Client1

## Slide 44
import java.io.*;
import java.net.*;
public class Server1 {
public static void main(String[] args){
try{
ServerSocket ss=new ServerSocket(6666);
Socket s=ss.accept();
DataInputStream din =
new DataInputStream(s.getInputStream());
String str=(String)din.readUTF();
System.out.println("Client: "+str);
din.close();
s.close();
ss.close();
}
catch(Exception e)
{System.out.println(e);}
}
}
import java.io.*;
import java.net.*;
public class Client1 {
public static void main(String[] args)
{
try{
Socket s=new Socket("localhost",6666);
DataOutputStream dout =
new DataOutputStream(s.getOutputStream());
dout.writeUTF("Hello Server");
dout.flush();
dout.close();
s.close();
}
catch(Exception e){System.out.println(e);}
}
}
Program 1: Sending data from a client to a server

## Slide 45: Program 1: Sending data from client to server
import java.io.*;
import java.net.*;
public class Server1 {
public static void main(String[] args){
try{
ServerSocket ss=new ServerSocket(6666);
Socket s=ss.accept();
DataInputStream dis =
new DataInputStream(s.getInputStream());
String str=(String)dis.readUTF();
System.out.println("Client says= "+str);
ss.close();
}
catch(Exception e)
{System.out.println(e);}
}
}
Server1.java

## Slide 46: Program 1: Sending data from client to server
import java.io.*;
import java.net.*;
public class Client1 {
public static void main(String[] args)
{
try{
Socket s=new Socket("localhost",6666);
DataOutputStream dout =
new DataOutputStream(s.getOutputStream());
dout.writeUTF("Hello Server");
dout.flush();
dout.close();
s.close();
}
catch(Exception e){System.out.println(e);}
}
}
Client1.java

## Slide 47: URL - Uniform Resource Locator
URL is a reference (an address) to a resource on the Internet.
  A resource can be a file, a database query and more.
URLs are just a subset of the more general concept of Uniform Resource Identifiers (URIs) which are meant to describe all points in the information space
  http://www.java.com:80/javaintro/index.html#Network
http
Protocol
www.java.com:
Host Name
80 javaintro/index.html
Port Number
javaintro/index.html
Path & File Name
  #Network
Reference

## Slide 48: Class URL
Class URL represents a Uniform Resource Locator, a pointer to a "resource" on the World Wide Web.
We distinguish between:
  Absolute URL - contains all of the information necessary to reach the resource.
  Relative URL - contains only enough information to reach the resource relative to (or in the context of) another URL.

## Slide 49: Constructors
URL(String urlSpecifier)
URL(URL urlObj, String urlSpecifier)
URL(String protName, String hostName, int port, String path)
URL(String protName, String hostName, String path)

## Slide 50: Commonly used methods of Java URL class
Method | Description
public String getProtocol() | Returns the protocol of the URL.
public String getHost() | Returns the host name of the URL.
public String getPort() | Returns returns the Port Number of the URL.
public String getFile() | Returns the file name of the URL.
public URLConnection openConnection() | Returns the instance of URLConnection i.e. associated with this URL.
public String getQuery() | Returns the query string of the URL.
public String toString() | Returns the string representation of the URL.
public String getDefaultPort() | it returns the default port of the URL.

## Slide 51: Example of Java URL class
import java.io.*;
import java.net.*;
public class URLDemo{
public static void main(String[ ] args){
try{
URL url=new URL("http://srpec.org.in/contacts");
System.out.println("Protocol: "+url.getProtocol());
System.out.println("Host Name: "+url.getHost());
System.out.println("Port Number: "+url.getPort());
System.out.println("File Name: "+url.getFile());
}
catch(Exception e){System.out.println(e);}
}
}

## Slide 52: Example
class URLDemo{
public static void main(String args[]) throws MalformedURLException
{
URL hp = new URL("http://content-ind.cricinfo.com/ci/content/current/story/news.html");
System.out.println("Protocol: " + hp.getProtocol());
System.out.println("Port: " + hp.getPort());
System.out.println("Host: " + hp.getHost());
System.out.println("File: " + hp.getFile());
System.out.println("Ext:" + hp.toExternalForm());
}
}

## Slide 53: Output
Protocol: http
Port: -1
Host: content-ind.cricinfo.com
File: /ci/content/current/story/news.html
Ext:http://content-ind.cricinfo.com/ci/content/current/story/news.html

## Slide 54: URLConnection class
The Java URLConnection class represents a communication link between the URL and the application.
This class can be used to read and write data to the specified resource referred by the URL.
The openConnection() method of URL class returns the object of URLConnection class.

## Slide 55: URLConnection class
URLConnection is an abstract class that represents an active connection to a resource specified by a URL.
The URLConnection class has two different but related purposes.
First, it provides more control over the interaction with a server (especially an HTTP server) than the URL class.
We can inspect the header sent by the server and respond accordingly. We can set the header fields used in the client request. We can use a URLConnection to download binary files.
URLConnection lets us send data back to a web server with POST or PUT and use other HTTP request methods.

## Slide 56: Process
Construct a URL object.
Invoke the URL object's openConnection( ) method to retrieve a URLConnection object for that URL.
Configure the URLConnection.
Read the header fields.
Get an input stream and read data.
Get an output stream and write data.
Close the connection.

## Slide 57: Reading Data from Server
Construct a URL object.
Invoke the URL object's openConnection( ) method to retrieve a URLConnection object for that URL.
Invoke the URLConnection's getInputStream( ) method.
Read from the input stream using the usual stream API.
The getInputStream() method returns a generic InputStream that lets you read and parse the data that the server sends.
public InputStream getInputStream( )

## Slide 58: Example
public class SourceViewer2 {
public static void main (String[] args) {
if (args.length > 0) {
try {
//Open the URLConnection for reading
URL u = new URL(args[0]);
URLConnection uc = u.openConnection( );
InputStream raw = uc.getInputStream( );
InputStream buffer = new BufferedInputStream(raw);
// chain the InputStream to a Reader
Reader r = new InputStreamReader(buffer);
int c;
while ((c = r.read( )) != -1)
{ System.out.print((char) c); }
}
catch (MalformedURLException ex) {
System.err.println(args[0]+" is not a parseable URL");
}
catch (IOException ex) {
System.err.println(ex);
}
} // end if
} // end main
} // end SourceViewer2

## Slide 59: URLConnection Example
import java.net.*;
import java.io.*;
public class URLConnectionReader {
public static void main(String[] args) throws Exception {
URL yahoo = new URL("http://www.yahoo.com/");
URLConnection yc = yahoo.openConnection();
BufferedReader in = new BufferedReader(
new InputStreamReader(
yc.getInputStream()));
String inputLine;
while ((inputLine = in.readLine()) != null)
System.out.println(inputLine);
in.close();
}
}

## Slide 60: Difference between URL and URLConnection
URLConnection provides access to the HTTP header.
URLConnection can configure the request parameters sent to the server.
URLConnection can write data to the server as well as read data from the server.

## Slide 61: Header Information
HTTP/1.1 200 OK
Date: Mon, 18 Oct 1999 20:06:48 GMT
Server: Apache/1.3.4 (Unix) PHP/3.0.6 mod_perl/1.17
Last-Modified: Mon, 18 Oct 1999 12:58:21 GMT
ETag: "1e05f2-89bb-380b196d"
Accept-Ranges: bytes
Content-Length: 35259
Connection: close
Content-Type: text/html

## Slide 62: Methods
public String getContentType( )
public int getContentLength( )
public long getDate( )
public long getExpiration( )
public long getLastModified( )

## Slide 63: Example
public class HeaderViewer {
public static void main(String args[]) { try {
URL u = new URL("http://www.rediffmail.com/index.html");
URLConnection uc = u.openConnection( );
System.out.println("Content-type: " +
uc.getContentType( ));
System.out.println("Content-encoding: "
+ uc.getContentEncoding( ));
System.out.println("Date: " + new Date(uc.getDate( )));
System.out.println("Last modified: "
+ new Date(uc.getLastModified( )));
System.out.println("Expiration date: "
+ new Date(uc.getExpiration( )));
System.out.println("Content-length: " +
uc.getContentLength( ));
} // end try
catch (MalformedURLException ex) {
System.out.println("I can't understand this URL...");
}
catch (IOException ex) {
System.err.println(ex);
}
System.out.println( );
} // end main
} // end HeaderViewer

## Slide 64: Sample Output
Sample output:
Content-type: text/htmlContent-encoding: nullDate: Mon Oct 18 13:54:52 PDT 1999Last modified: Sat Oct 16 07:54:02 PDT 1999Expiration date: Wed Dec 31 16:00:00 PST 1969 Content-length: -1
Sample output for: http://www.oreilly.com/graphics/space.gif
Content-type: image/gifContent-encoding: nullDate: Mon Oct 18 14:00:07 PDT 1999Last modified: Thu Jan 09 12:05:11 PST 1997Expiration date: Wed Dec 31 16:00:00 PST 1969 Content-length: 57

## Slide 65: Retrieving Header field
public String getHeaderField(String name)
Example:
  String contentType = uc.getHeaderField("content-type");
  String contentEncoding = uc.getHeaderField("content-encoding"));
  String data = uc.getHeaderField("date");
  String expires = uc.getHeaderField("expires");
  String contentLength = uc.getHeaderField("Content-length");

## Slide 66: Datagrams
A datagram is an independent, self-contained message sent over the network whose arrival, arrival time, and content are not guaranteed.
The java.net package contains three classes to help you write Java programs that use datagrams to send and receive packets over the network: DatagramSocket and DatagramPacket

## Slide 67: TCP vs. UDP

## Slide 68: UDP in Java
DatagramPacket
DatagramSocket

## Slide 69: Receiving DatagramPacket
public DatagramPacket(byte[] buffer, int length)
public DatagramPacket(byte[] data, int offset, int length, InetAddress destination, int port)
public DatagramPacket(byte[] buffer, int offset, int length)
  Example:
  byte[] buffer = new byte[8192];
  DatagramPacket dp = new
  DatagramPacket(buffer, buffer.length);

## Slide 70: Sending Datagrams
DatagramPacket(byte[] barr, int length):
  Creates a datagram packet. This constructor is used to receive the packets.
DatagramPacket(byte[] barr, int length, InetAddress address, int port):
  Creates a datagram packet. This constructor is used to send the packets.

## Slide 71: DatagramSocket
public DatagramSocket( ) throws SocketException
public DatagramSocket(int port) throws SocketException
public DatagramSocket(int port, InetAddress interface) throws SocketException

## Slide 72: Sending and Receiving Packets
public void send(DatagramPacket dp) throws IOException
public void receive(DatagramPacket dp) throws IOException

## Slide 73: DatagramSocket Class
Methods

## Slide 74
Method | Description
void bind(SocketAddress addr) | Binds the DatagramSocket to a specific address and port.
void connect(InetAddress address, int port) | Connects the socket to a remote address for the socket.
void send(DatagramPacket p) | Sends the datagram packet from the socket.
void receive(DatagramPacket p) | Receives the datagram packet from the socket.
void disconnect() | Disconnects the socket.
void close() | Closes the datagram socket.
DatagramChannel getChannel() | Returns a unique DatagramChannel object associated with the datagram socket.
InetAddress getInetAddress() | Returns the address to where the socket is connected.
InetAddress getLocalAddress() | Gets the local address to which the socket is connected.
int getLocalPort() | Returns the port number on the local host to which the socket is bound.
int getPort() | Returns the port number to which the socket is connected.
boolean isClosed() | Returns the status of socket i.e. closed or not.
boolean isConnected() | Returns the connection state of the socket.

## Slide 75: DatagramPacket Class
Methods

## Slide 76: Example:
UDPServer
UDPClient